## Slide 1: Bobcats on the Moon Demonstrating an MSU Built Computer on the Lunar Surface
Dr. Brock J. LaMeres Professor, Electrical & Computer Engineering
Director, MT Engineering Education Research Center
Boeing Professor of Engineering Education

## Slide 2: What I’d Like to Talk About Today
What is Research and Why do it at Universities

## Slide 3: What I’d Like to Talk About Today
What is Research and Why do it at Universities
My Research on Computers

## Slide 4: What I’d Like to Talk About Today
What is Research and Why do it at Universities
My Research on Computers
3) The RadPC Project

## Slide 5: What is Research?
Creation of Knowledge
  Something that benefits society, but is 5-20 years down the road.
  High risk, high reward.
  A company couldn’t do it and stay in business.
  STEM innovations fuel our economy.

## Slide 6: What is Research?
Creation of Knowledge
  Something that benefits society, but is 5-20 years down the road.
  High risk, high reward.
  A company couldn’t do it and stay in business.
  STEM innovations fuel our economy.
Where does the Money Come From?
  You! We all pay taxes.
  ~$150B total of $4T Federal Budget Goes to Research
    Defense = $50B
    National Institute of Health = $35B
    Energy = ~$15B
    NASA = ~$10B
    National Science Foundation = ~$6B

## Slide 7: What is Research?
Creation of Knowledge
  Something that benefits society, but is 5-20 years down the road.
  High risk, high reward.
  A company couldn’t do it and stay in business.
  STEM innovations fuel our economy.
Where does the Money Come From?
  You! We all pay taxes.
  ~$150B total of $4T Federal Budget Goes to Research
    Defense = $50B
    National Institute of Health = $35B
    Energy = ~$15B
    NASA = ~$10B
    National Science Foundation = ~$6B
Why do Research at Universities?
  We do have national labs (PNNL, LANL, etc).
  Universities can sustain knowledge when funding lapses.
  And we have students to do the work!

## Slide 8: Brock’s Computer Research
Can you image life without a computer?
  What images do you conjure when someone says “computer”?

## Slide 9: Brock’s Computer Research
Can you image life without a computer?
  What images do you conjure when someone says “computer”?
  There were ~400M personal computers sold in 2018.
  There were ~1.5B smart phones being sold (1.3B Android, rest iOS).

## Slide 10: Brock’s Computer Research
Can you image life without a computer?
  What images do you conjure when someone says “computer”?
  There were ~400M personal computers sold in 2018.
  There were ~1.5B smart phones sold in 2018 (1.3B Android, 1.5B iOS).
But what about these things?

## Slide 11: Brock’s Computer Research
Can you image life without a computer?
  What images do you conjure when someone says “computer”?
  There were ~400M personal computers sold in 2018.
  There were ~1.5B smart phones sold in 2018 (1.3B Android, 1.5B iOS).).
But what about these things?
  There were 25B embedded computers sold in 2018.

## Slide 12: Brock’s Computer Research
Our Existing Computers Work Well. What’s the Problem?

## Slide 13: Brock’s Computer Research
Our Existing Computers Work Well. What’s the Problem?
  Our existing computers have benefited from 40+ years of Moore’s Law.
  In the 1960’s, Gordon Moore predicted that the number of transistors on a chip would double every ~24 months.
Gordon Moore, co-founder of Intel, holding a vacuum tube.
1959 - 1965
1971* - 2011
Note: First microprocessor introduced in 1971,
the Intel 4004 with 2300 transistors.

## Slide 14: Brock’s Computer Research
Why is Moore’s Law so Cool?
  Our general-purpose computer model has gotten smaller, faster, and more power efficient every 24 months.
  This has allowed faster operation and more sophisticated software to be executed. and prevented any major overhaul in the way we do things…
Replica of the First Transistor
(Source: AP Photo Paul Sakuma)
Intel Xeon Phi, 22nm
(Source: newsroom.intel.com)
Intel 4004, 10um
(Source: newsroom.intel.com)
1947 (1 transistor)
1971 (2300 transistors)
2012 (5B transistors)
2019 (15B transistors)
NVIDIA Pascal GPU
(Source: invidia.com)

## Slide 15: Brock’s Computer Research
When will Moore’s Law End?
  Most exponentials do come to an end.
Clock Speed
Power
Performance per Clock Cycle

## Slide 16: Brock’s Computer Research
When will Moore’s Law End?
  Most exponentials do come to an end.
Clock Speed
Power
Performance per Clock Cycle
So it’s over?

## Slide 17: Brock’s Computer Research
Moore’s Law Wasn’t the First Exponential, and Won’t be the Last…
You Are Here

## Slide 18: Brock’s Computer Research
Reconfigurable Computing
The typical approach to computer hardware is to build everything that will ever be needed.
Then the software can decide what to use later.

## Slide 19: Brock’s Computer Research
Reconfigurable Computing
The typical approach to computer hardware is to build everything that will ever be needed.
Then the software can decide what to use later.
What if the hardware could be changed based on the application?

## Slide 20: Brock’s Computer Research
Today’s Computers are Based on a General-Purpose Processor
  The GP CPU is designed to do many things.
  This is the “Jack of All Trades, Master of None” approach.
General Purpose CPU Model

## Slide 21: Brock’s Computer Research
Today’s Computers are Based on a General-Purpose Processor
  The GP CPU is designed to do many things.
  This is the “Jack of All Trades, Master of None” approach.
General Purpose CPU Model
Reconfigurable Computing Model
This can be faster because the hardware is smaller and consumes less power.

## Slide 22: Brock’s Computer Research
So off to work…
  We started investigating computational speedup by swapping in HW in real-time.

## Slide 23: Brock’s Computer Research
But then…
Hey, that’s pretty cool. That might help our space computers.

## Slide 24: Brock’s Computer Research
The Promise of RC
  We discovered that space computers could be greatly enhanced by RC.
  They need to be light. RC reuses hardware, that saves mass.

## Slide 25: Brock’s Computer Research
The Promise of RC
  We discovered that space computers could be greatly enhanced by RC.
  They need to be light. RC reuses hardware, that saves mass.

## Slide 26: Brock’s Computer Research
The Promise of RC
  We discovered that space computers could be greatly enhanced by RC.
  They need to be light. RC reuses hardware, that saves mass.
  They need to be low power. RC eliminates unnecessary circuitry.

## Slide 27: Brock’s Computer Research
The Promise of RC
  We discovered that space computers could be greatly enhanced by RC.
  They need to be light. RC reuses hardware, that saves mass.
  They need to be low power. RC eliminates unnecessary circuitry.

## Slide 28: Brock’s Computer Research
The Promise of RC
  We discovered that space computers could be greatly enhanced by RC.
  They need to be light. RC reuses hardware, that saves mass.
  They need to be low power. RC eliminates unnecessary circuitry.
  They need to have high computation. RC can do that.

## Slide 29: Brock’s Computer Research
The Promise of RC
  We discovered that space computers could be greatly enhanced by RC.
  They need to be light. RC reuses hardware, that saves mass.
  They need to be low power. RC eliminates unnecessary circuitry.
  They need to have high computation. RC can do that.

## Slide 30: Brock’s Computer Research
The Promise of RC
  We discovered that space computers could be greatly enhanced by RC.
  They need to be light. RC reuses hardware, that saves mass.
  They need to be low power. RC eliminates unnecessary circuitry.
  They need to have high computation. RC can do that.
  They need to operate in the presence of harsh radiation.

## Slide 31: Brock’s Computer Research
The Promise of RC
  We discovered that space computers could be greatly enhanced by RC.
  They need to be light. RC reuses hardware, that saves mass.
  They need to be low power. RC eliminates unnecessary circuitry.
  They need to have high computation. RC can do that.
  They need to operate in the presence of harsh radiation.
Can you repeat the question???

## Slide 32: Brock’s Computer Research
The Space Radiation Environment
Nuclear Fusion

## Slide 33: Brock’s Computer Research
The Space Radiation Environment

## Slide 34: Brock’s Computer Research
Radiation Effect on Electronics
1) Total Ionizing Dose (TID)
- Material Damage

## Slide 35: Brock’s Computer Research
Radiation Effect on Electronics
1) Total Ionizing Dose (TID)
- Material Damage
2) Single Event Effects (SEEs) - Bit Flips

## Slide 36: Brock’s Computer Research
If this radiation is a problem, how do our computers work now?

## Slide 37: Brock’s Computer Research
You Are Here

## Slide 38: Brock’s Computer Research
Van Allen Belts – Trapped Radiation Around Earth

## Slide 39: Brock’s Computer Research
The Atmosphere Attenuates What Gets Through the Magnetosphere
You Are Here

## Slide 40: Brock’s Computer Research
But There are Computers in Space Now?

## Slide 41: Brock’s Computer Research
Existing Space Processors are “Radiation Hardened”
  Custom Materials & Design Approaches

## Slide 42: Brock’s Computer Research
Well then, the problem is solved, right?

## Slide 43: Brock’s Computer Research
Well then, the problem is solved, right?
  They can get expensive.
A Rad-Hard Processor can cost $200k.
Mars Curiosity has 2 (Side A and Side B)

## Slide 44: Brock’s Computer Research
Well then, the problem is solved, right?
  They can get expensive.
  They are also slow.
- Rad-Hardened Processers lag in performance to their commercial counterparts by ~10 years

## Slide 45: Brock’s Computer Research
Space Computing Needs
  NASA Technology Area 11 – Flight Computing
    Increased Computation
    Radiation hardened technologies
    Low power requirements
    Cost Feasible
This is the new variable

## Slide 46: MSU’s Approach - RadPC
A Fault Tolerant, Reconfigurable Computer
  Use a COTS Field Programmable Gate Array (FPGA). Hardware is Reconfigurable. Cost is low.

## Slide 47: MSU’s Approach - RadPC
A Fault Tolerant, Reconfigurable Computer
  Use a COTS Field Programmable Gate Array (FPGA). Hardware is Reconfigurable. Cost is low.
  Use a modern part with <65nm process node to achieve TID tolerance. (~600krad)

## Slide 48: MSU’s Approach - RadPC
A Fault Tolerant, Reconfigurable Computer
  Use a COTS Field Programmable Gate Array (FPGA). Hardware is Reconfigurable. Cost is low.
  Use a modern part with <65nm process node to achieve TID tolerance. (~600krad)
  Triplicated Cores + Spares for SEE tolerance.
    3 Tiles run in TMR with spares in reset.
9 MicroBlaze Processors on Artix-7
Precedent: Shuttle Flight Computer (TMR + Spare)

## Slide 49: MSU’s Approach - RadPC
A Fault Tolerant, Reconfigurable Computer
  Use a COTS Field Programmable Gate Array (FPGA). Hardware is Reconfigurable. Cost is low.
  Use a modern part with <65nm process node to achieve TID tolerance. (~600krad)
  Triplicated Cores + Spares for SEE tolerance.
    3 Tiles run in TMR with spares in reset.
  Spatial Avoidance and Background Repair
    If TMR detects a fault, the damaged tile is replaced with a spare and foreground operation continues
    The tile is “repaired” in the background via partial reconfiguration (PR).
9 MicroBlaze Processors on Artix-7
Precedent: Shuttle Flight Computer (TMR + Spare)

## Slide 50: MSU’s Approach - RadPC
A Fault Tolerant, Reconfigurable Computer
  Use a COTS Field Programmable Gate Array (FPGA). Hardware is Reconfigurable. Cost is low.
  Use a modern part with <65nm process node to achieve TID tolerance. (~600krad)
  Triplicated Cores + Spares for SEE tolerance.
    3 Tiles run in TMR with spares in reset.
  Spatial Avoidance and Background Repair
    If TMR detects a fault, the damaged tile is replaced with a spare and foreground operation continues
    The tile is “repaired” in the background via partial reconfiguration (PR).
  Scrubbing
    Blind scrubbing continually runs through tiles (fast)
    Readback scrubbing periodically runs through rest of fabric (slower)
9 MicroBlaze Processors on Artix-7
Precedent: Shuttle Flight Computer (TMR + Spare)

## Slide 51: MSU’s Approach - RadPC
Why do it this way?
  With Spares, it basically becomes a flow-problem:
      TMR produces the right output, but repair is inevitable.
      Partial Reconfiguration is faster than Full Reconfiguration.
      Brining on a spare is faster than Partial Reconfiguration.
      If the repair rate is faster than the incoming fault rate, you’re safe.
      If the repair rate is slightly slower than the incoming fault rate, spares give you additional time.
      The additional time can accommodate varying flux rates.
      Abundant resources on an FPGA enable dynamic scaling of the number of spares. (e.g., build a bigger tub in real time)

## Slide 52: MSU’s Approach - RadPC
Modeling: Is this an improvement to TMR+Srubbing?
  We use a Markov Model to predict Mean-Time-Before-Failure.
  We want to see if it improves MTBF over non-redundant & TMR+scrubbing.
  The fault rate was extracted from CREME96 for 4 different orbits for Virtex-6 FPGA.
  The repair rate was found empirically.
ISS
HEO
HRBE
GEO

## Slide 53: MSU’s Approach - RadPC
Modeling: Is this an improvement to TMR+Srubbing?
  We use a Markov Model to predict Mean-Time-Before-Failure.
  We want to see if it improves MTBF over non-redundant & TMR+scrubbing.
  The fault rate was extracted from CREME96 for 4 different orbits for Virtex-6 FPGA.
  The repair rate was found empirically.
ISS
HEO
HRBE
GEO
Ok, it looks promising.

## Slide 54: MSU’s Approach - RadPC
Technical Readiness Level (TRL)

## Slide 55: MSU’s Approach - RadPC
Step 1 – Build a Prototype to See if it is Possible
  The Montana Space Grant Consortium funds an investigation into conducting radiation tolerant computing research at MSU. The goal is to understand the problem, propose a solution, and build relationships with scientists at NASA.
(2008-2010)
Proof of Concept
Timeline of Activity at MSU
Clint Gauer (MSEE from MSU 2009) demo’s computer to MSFC Chief of Technology Andrew Keys
2010
2011
2012
2013
2014-16
2016
2017-20
2009
2008

## Slide 56: MSU’s Approach - RadPC
Step 2 –Test in a Cyclotron
  NASA EPSCoR funds the development of a more functional prototype and testing under bombardment by radiation at the Texas A&M Radiation Effects Facility.
(2008-2010)
Proof of Concept
Prototype Development & Cyclotron Testing
(2010-2012)
Timeline of Activity at MSU
Ray Weber (Ph.D., EE from MSU, 2014) prepares experiment.
2010
2011
2012
2013
2014-16
2016
2009
2008
MSU Computer
2017-20

## Slide 57: MSU’s Approach - RadPC
Step 3 – Demonstrate as Flight Hardware on High Altitude Balloons
  NASA Education Office funds the development of the computer into flight hardware for demonstration on high altitude balloon systems, both in Montana and at NASA.
(2008-2010)
Proof of Concept
Prototype Development & Cyclotron Testing
High Altitude Balloon Demos
(2010-2012)
(2011-2013)
Timeline of Activity at MSU
MSU Computer
Justin Hogan (Ph.D., EE from MSU, 2014) prepares payload.
2010
2011
2012
2013
2014-16
2016
2009
2008
2017-20

## Slide 58: MSU’s Approach - RadPC
Step 4 – Demonstrate as Flight Hardware on a Sounding Rocket
  NASA OCT & FOP fund the demonstration of the computer system on sounding rocket.
  Flew on UP Aerospace SpaceLoft-9 in Oct 2014.
(2008-2010)
Proof of Concept
Prototype Development & Cyclotron Testing
High Altitude Balloon Demos
Sounding Rocket Demo
(2010-2012)
(2011-2013)
(2012-2016)
Timeline of Activity at MSU
2010
2011
2012
2013
2014-16
2016
2009
2008
MSU Computer
2017-20

## Slide 59: MSU’s Approach - RadPC
Step 5 – Demonstrate on the International Space Station
  NASA EPSCoR funds the demonstration of computer system on ISS
(2008-2010)
Proof of Concept
Prototype Development & Cyclotron Testing
High Altitude Balloon Demos
Sounding Rocket Demo
ISS
Demo
(2010-2012)
(2011-2013)
(2012-2016)
(2014-2016)
Timeline of Activity at MSU
2010
2011
2012
2013
2014-16
2016
2009
2008
2017-20

## Slide 60: MSU’s Approach - RadPC
Step 6 – Demonstrate as a Stand-Alone Satellite
  NASA SmallSat Technology Partnership Program (SSTP) funds the planning for a stand-alone satellite demonstration of the computer technology.
  NASA Undergraduate Student Instrument Program (USIP) funds a team of undergraduates to build the satellite and prepare for deployment.
  NASA CubeSat Launch Initiative (CSLI) selects RadSat-g for launch on ELaNa-23 mission on CRS-OA9.
  NASA ISS EPSCoR funds building the flight unit, delivering to the launch provider, and operating the satellite post-deployment.
(2008-2010)
2010
2011
2012
2013
2014-16
2016
Proof of Concept
Prototype Development & Cyclotron Testing
High Altitude Balloon Demos
Sounding Rocket Demo
ISS
Demo
Satellite
Demo
(2010-2012)
(2011-2013)
(2012-2016)
(2014-2016)
(2015-2020)
2009
2008
Timeline of Activity at MSU
2017-20

## Slide 61: MSU’s Approach - RadPC
RadSat Mission Concept
Students Build It

## Slide 62: MSU’s Approach - RadPC
RadSat Mission Concept
Students Build It
Launch it to the International Space Station

## Slide 63: MSU’s Approach - RadPC
RadSat Mission Concept
Students Build It
Launch it to the International Space Station
Put into Orbit using NanoRacks CubeSat Deployer

## Slide 64: MSU’s Approach - RadPC
In case you didn’t see that…

## Slide 65: MSU’s Approach - RadPC
In case you didn’t see that…

## Slide 66: MSU’s Approach - RadPC
In case you didn’t see that…

## Slide 67: MSU’s Approach - RadPC

## Slide 68: MSU’s Approach - RadPC

## Slide 69: MSU’s Approach - RadPC
RadSat Mission Concept
Students Build It
Launch it to the International Space Station
Put into Orbit using NanoRacks CubeSat Deployer
Operate from SSEL Ground Station

## Slide 70: MSU’s Approach - RadPC
RadSat Mission Concept
- There are two RadSats
In orbit now
With NASA, launches Oct 21, 2019

## Slide 71: MSU’s Approach - RadPC
How do you do all this?

## Slide 72: MSU’s Approach - RadPC
Everything was Designed & Built By MSU Students (~150)
Todd Buerkle, Justin Hogan, Ray Weber at Johnson Space Center for demo, 2012.
Todd Buerkle, Jennifer Hane at the Marshall Space Flight Center, 2011.
Justin Hogan at the NASA Columbia Scientific Balloon Facility, 2012.
Justin Hogan & Ray Weber featured in MSU News Story, 2012.
Clint Gauer demo’s computer at Marshall Space Flight Center, 2009.
Todd Buerkle & Jennifer Hane demo computer at Marshall Space Flight Center, 2012.
Clint Gauer at Marshall Space Flight Center for demo, 2009.
Kaysha Young prepares payload for balloon flight, 2012.
2013 balloon team recovers payload in front of moose, 2013.
2011 balloon team featured in MSU news story, 2011.

## Slide 73: MSU’s Approach - RadPC
Now What?

## Slide 74: Bobcats on the Moon

## Slide 75: Bobcats on the Moon
The NASA Concept for Lunar Exploration

## Slide 76: Bobcats on the Moon
The NASA Concept for Lunar Exploration

## Slide 77: Bobcats on the Moon
The NASA Concept for Lunar Exploration
MSU is going to be part of this.

## Slide 78: Bobcats on the Moon
How are you going to pull this off?

## Slide 79: Bobcats on the Moon
With MSU Students!

## Slide 80: Questions
MSU Computer
MSU Computer
MSU Computer
MSU Computer
MSU Computer

## Slide 81: Backup Slides

## Slide 82: Quick Background of MSU
Space Science & Engineering Lab
Founded in 2000 with support from MSGC.
Provides students hands-on experience w/ real space missions.
One of the first universities to engage in small satellites (part of the inaugural ELaNa-I).
Has sent 9 small satellites into space (10 & 11 within next 6 months.)

## Slide 83: Professor Reflections
The Pros…
  Fantastic experience for students.
  They are HIGHLY recruited.
  High profile for the university.
The Cons…
  Graduation kills productivity. (the experience often displaces results)
  Keeping funding going is piecemeal and exhausting. (The work I showed represents 14 different grants)
  NASA schedules don’t match academic calendars.
The Box Score
  It’s worth it!

## Slide 84: References
KFF Medicare Report: https://www.kff.org/medicare/issue-brief/the-facts-on-medicare-spending-and-financing/