## Slide 1: Simulating Spatial Hearing Cues With Digital Signal Processing
Robert C. Maher, Ph.D.
Digital Audio Signal Processing Lab

## Slide 2: Outline
What does “spatial hearing” mean?
Some basics of acoustics
Characteristics of human hearing
Simulating natural acoustical environments with digital processing
Some examples

## Slide 3: Spatial Hearing
The brain interprets the sound waves arriving at each ear in order to deduce the direction and distance of a sound source.
The brain can also estimate the size, shape, orientation, and relative motion of the source, as well as the size and composition of the surrounding space.

## Slide 4: Spatial Hearing
Sound Source

## Slide 5: Basics of Acoustics
Sound propagates through air as a longitudinal wave
Speed of sound:
  343 m/s @ 20°C (331 m/s @ 0°C)
  About 1125 ft/s (5 seconds per mile)
  About 1 ft/ms (light travels about 1 ft/ns)
Audible wavelengths: 1.7cm to 17m

## Slide 6: Human Hearing Characteristics
Frequency sensitivity roughly 20 Hz – 20kHz
  3 decades, or 10 octaves
  Compares to less than one octave for human visual system (wavelengths: 3800 – 7600 angstroms)
Amplitude sensitivity roughly 20Pa – 20Pa
  Atmospheric pressure: 105 Pa
  Minimum audible sound corresponds to motion a fraction of diameter of hydrogen atom!
Difference judgments good, absolute judgments poor

## Slide 7: Basics of Spatial Hearing
Two ears: stereo measurements
  Interaural time difference (ITD)
    Effective below about 1.5kHz
  Interaural intensity difference (IID)
    Effective above about 1.5kHz
Learned experience with pinnae, head diffraction, reflections and reverberation

## Slide 8: Spherical Frame of Reference
Azimuth (top view)

+
-
F
+
-
Elevation (side view)

## Slide 9: Interaural Differences
S()
A()
LE()
RE()
Sound Source
ITD = (d/c)*(+ sin())
IID due to “head shadow”
d

Ipsilateral = ear on same side as source
Contralateral = ear on opposite side as source

## Slide 10: Transfer Function
Linear Time-Invariant (LTI) systems can be fully described by an impulse response
Fourier Transform of the impulse response is the transfer function
Acoustical path from a sound source to the listener’s ear is LTI, so we can describe the acoustical system with a transfer function

## Slide 11: Diffraction and Pinna Effects: Head-Related Transfer Function
HRTF measured by placing a probe microphone into ear canal to record the impulse response from source to eardrum
HRTF varies with azimuth and elevation: must take a lot of measurements

## Slide 12: Anatomical details are important:
HRTFs differ from one individual to another…

## Slide 13: HRTF Characteristics

## Slide 15: Reflections and Reverberation
Direct sound arrival is followed by reflections from room surfaces
Overlapping reflections are heard as reverberation
Direct-to-Reverberant ratio gives cues to size of room, type of room surfaces, and distance from source

## Slide 16: Simulation of Acoustic Environment with DSP
Start with monophonic sound source
Calculate geometry and HRTFs
Process source signal with acoustic transfer functions
Compensate for playback system (headphones or loudspeakers)

## Slide 17: Cross Talk Cancellation
How to get left signal only to left ear and right signal only to right ear when using speakers?
Audio Inputs
Speakers
L()
R()
Cross Talk Compensation
Network
LP()
RP()
S()
S()
A()
A()
LE()
RE()
LP
RP

## Slide 18: Second-Order Effects
Simulate Doppler frequency shift for moving sources
Take into account the directional characteristics of the source
Calculate reflections and reverberation

## Slide 19: Audio Examples
Example 1
  Spatial drums
  Circling sounds
Example 2
  Soundtrack for action computer game
Example 3
  Spatialized enhancement (single-ended process)

## Slide 20: Significant Applications
“Auralization” of acoustical environments
Entertainment
  music production, computer games, movie soundtracks
“Immersive” simulation and training systems
  military, aerospace, and law enforcement
Improved detectability and intelligibility of audible warning and communication signals